Zilog asz280 Assembler
(for Z80/Z180/Z280)

Overview:

The asz280 assembler was developed within the assembler suite for small systems by Alan R. Baldwin, ASxxxx version 5.20. The assembler was derived from his Z80 version, asz80, but is table-driven, and shares little code anymore with that assembler. It uses the code common to all of his assemblers (asxsrc) without modification. This assembler is freely distributed under the GNU Public License, version 3, available at:

http://www.gnu.org/licenses/gpl.html

Instruction Sets:

A number of assembler directives control which instructions may be used within a section of code. One may freely switch between instruction sets by multiple uses of the following directives.

.z80	Default; only instructions for the Z80 may be used
.z180	The instruction set is expanded to include both Z80 and Z180	instructions.
.z280	z280 instructions and addressing modes may be used. Note	that only User Mode instructions are in this set; privileged z280	instructions may not be used. Certain z80 instructions (such as	IM n) are privileged on the z280 and may not be used.

Three specialized instruction sets may be enabled; viz.,

.z280p	z280 Privileged Instructions may be assembled. This also	enables the z80 instructions that are privileged on the z280.	This is the broadest category of instructions, such as would be	used for supervisor programming.
.z280n	No I/O. Since user programs on the z280 may be restricted	from using I/O instructions, this assembly mode prevents their	use. This includes placing z80 I/O instructions off-limits, too.
.z80u	Enables z80 undocumented instructions. The set of	instructions enabled by this directive may not be complete as of	the first release of the assembler.

Addressing Mode Syntax:

DA – direct address (all)

Direct addresses are enclosed in parentheses, and may include expressions; e.g.,

data:	.dw	0x25

ld	a,(data)

Exceptions:
call	subr
jp	label
djnz	label2

SX – short index (all)

ld	a,50(ix)	; SDCC compatible
ld	a,(iy-25)	; asz280 syntax

Familiar to z80 programmers, indexing is off of the IX or IY register, and indices may be in the range [-128..+127]. The first form may be an expression, but it must not begin with a left paren. If parentheses are needed, use:

ld	a,0+(expression)(ix)

The second form requires that the index register be the first term after the opening left paren.

LX – long index (z280) (‘X’ in the 280 manual)

ld	a,5000(ix)
ld	a,(iy-0x480)
ld	a,4000(hl)
ld	a,(hl+01000)	;octal offset

Many, but not all, z280 instructions allow indexing using the HL register. LX addresses are distinguished by the magnitude of the offset. If the HL register is used, the magnitude of the offset is not significant. Likewise, if the second form is used, the index register must be the first term after the opening left paren.

SR – stack relative (z280)

add	a,(sp+0x224)
ld	a,0x224(sp)
sbc	a,(sp)	;offset is 0000

All indices are taken as signed word offsets.
RA – relative addresses (z280)

Relative addresses are used on the Z80 for certain instructions:

djnz	label
jr	[cond,] label

The label offset is computed from the location counter after the instruction.

Relative addresses on the z280 may be used almost anywhere DA, LX, or SR addressing is permitted. Examples:

ld	a,[data+20]
jp	[label]
call	[subr]

Relative addresses are distinguished by the use of square brackets, instead of parentheses. All offsets are calcuted from the beginning of the instruction following the one using the relative address. Relative address usage with the JP instruction is useful for extending the range of a JR to a long offset. Example,

jp	nc,label	;direct address, require relocation
jr	nc,label	;relative always, no relocation

jp	nc,[label]	;specifically relative, longer
; range than JR

Relative addressing may be use with external code references, such as:

.globl	ext_subr

call	[ext_subr]	;offset filled in by aslink

References:

1. ASxxxx Cross Assemblers – Alan R. Baldwin
2. Preliminary Technical Manual, Z280 MPU Microprocessor Unit, Zilog, 1989.